Specifications of 15 ton/day Seawater Fluidic Ice Machine

a). Parameters

| NO. | Name | Data | Remarks |
| --- | --- | --- | --- |
| 1. Designed Working condition |
| 1.1 | Standard Ambient temperature | 25 ℃ |  |
| 1.2 | Inlet water temperature | 18 ℃ |  |
| 1.3 | Water requirement | Seawater | Fresh water is no allowed |
| 1.4 | Power Supply | 380V, 3Ph, 50Hz |  |
| 2. General Performance Parameters |
| 2.1 | Ice marking capacity(daily) | 15ton/day |  |
| 2.2 | Content of ice crystal: | 40% |  |
| 2.3 | Cooling capacity | 35kW |  |
| 2.4 | Evaporating temperature | -15 ℃ |  |
| 2.5 | Condensing temperature | +40 ℃ |  |
| 2.6 | Refrigerant | R404A |  |
| 2.7 | Compressor input power | 18kW |  |
| 2.8 | Ice knife motor input | 3kW |  |
| 2.9 | Water pump input | 0.2 kW |  |
| 2.10 | Condenser pump input | 3 kW | Customer supplied |
| 2.12 | Total Power | 24.5 kW |  |
| 2.13 | Total Dimension(L*W*H) (mm) | 1450×1200×1700 |  |
| 2.14 | Total weight | 1400 kg |  |

b). Parts list

| NO. | Item/ Description | Brand | Qty | Remarks |
| --- | --- | --- | --- | --- |
| Refrigeration Unit |
| 1 | Compressor | Bitzer | 1 |  |
| 2 | Dual pressure controller | Saginomiya | 1 |  |
| 3 | Water Condenser | Aoxin | 1 |  |
| 4 | Dry filter | Danfoss | 1 |  |
| 5 | Sight glass | Danfoss | 1 |  |
| 6 | Solenoid valve | Danfoss | 1 |  |
| 7 | Expansion valve | Danfoss | 1 |  |
| 8 | Evaporator | Jiangnan | 1 |  |
|  | Reducer with motor | Taixing | 1 |  |
|  | Ice Drum | Jiangnan | 1 |  |
|  | Ice Knife | Jiangnan | 1 |  |
| 9 | Water Tank | Jiangnan | 1 |  |
| 10 | Water pump | Resun | 1 |  |
| 11 | Suction filter | Carly | 1 |  |
| 12 | Water flow meter |  | 1 |  |
| Electrical parts |
| 1 | Electrical Box |  | 1 |  |
| 2 | circuit breaker |  | 1 |  |
| 3 | Contactor | Telemecanique | 3 |  |
| 4 | Thermal relay | Telemecanique | 3 |  |
| 5 | Relay | Omron | 1 |  |

Specifications 25 ton/day Seawater Fluidic Ice Machine

a). Parameters

| NO. | Name | Data | Remarks |
| --- | --- | --- | --- |
| 1. Designed Working condition |
| 1.1 | Standard Ambient temperature | 25 ℃ |  |
| 1.2 | Inlet water temperature | 18 ℃ |  |
| 1.3 | Water requirement | Seawater | Fresh water is no allowed |
| 1.4 | Power Supply | 380V, 3Ph, 50Hz |  |
| 2. General Performance Parameters |
| 2.1 | Ice marking capacity(daily) | 25ton/day |  |
| 2.2 | Content of ice crystal: | 40% |  |
| 2.3 | Cooling capacity | 60kW |  |
| 2.4 | Evaporating temperature | -15 ℃ |  |
| 2.5 | Condensing temperature | +40 ℃ |  |
| 2.6 | Refrigerant | R404A |  |
| 2.7 | Compressor input power | 28W |  |
| 2.8 | Ice knife motor input | 6kW |  |
| 2.9 | Water pump input | 0.5 kW |  |
| 2.10 | Condenser pump input | 4 kW | Customer supplied |
| 2.12 | Total Power | 36 kW |  |
| 2.13 | Total Dimension(L*W*H) (mm) | 2100×1800×1800 |  |
| 2.14 | Total weight | 2500 kg |  |

b). Parts list

| NO. | Item/ Description | Brand | Qty | Remarks |
| --- | --- | --- | --- | --- |
| Refrigeration Unit |
| 1 | Compressor | Bitzer | 1 |  |
| 2 | Dual pressure controller | Saginomiya | 1 |  |
| 3 | Water Condenser | Aoxin | 1 |  |
| 4 | Dry filter | Danfoss | 1 |  |
| 5 | Sight glass | Danfoss | 1 |  |
| 6 | Solenoid valve | Danfoss | 1 |  |
| 7 | Expansion valve | Danfoss | 2 |  |
| 8 | Evaporator | Jiangnan | 2 |  |
|  | Reducer with motor | Taixing | 2 |  |
|  | Ice Drum | Jiangnan | 2 |  |
|  | Ice Knife | Jiangnan | 2 |  |
| 9 | Water Tank | Jiangnan | 1 |  |
| 10 | Water pump | Resun | 1 |  |
| 11 | Suction filter | Carly | 1 |  |
| 12 | Water flow meter |  | 1 |  |
| Electrical parts |
| 1 | Electrical Box |  | 1 |  |
| 2 | circuit breaker |  | 1 |  |
| 3 | Contactor | Telemecanique | 3 |  |
| 4 | Thermal relay | Telemecanique | 3 |  |
| 5 | Relay | Omron | 1 |  |